## Slide 1: GMV/ISON COMBINED OPTICAL CAMPAIGNS
ESDC 2017
April 20th 2017, ESOC
D. Escobar, PhD
F. Ayuga
A. Antón
A. Águeda
I. Molotov

## Slide 2: Outline
  ISON telescope network
  GMV/ISON campaigns
  Use cases:
    Orbit determination
    Ranging station calibration
    Collision risk evaluation
    End-of-life operations

## Slide 3: ISON telescope network
  World-wide coverage, with telescopes in both hemispheres
  High-availability thanks to high number of telescopes with de-correlated weather conditions
  High-accuracy of optical data (~ 1 arcsec)
  High number of both survey and tracking telescopes (>90)
  ISON sub-network devoted to provide commercial services
  Use for operational support in various scenarios
    Orbit determination with data fusion
    Ranging station calibration
    Collision risk evaluation
    LEOP, IOT, EOL, contingency, …
    World-map of ISON telescope network

## Slide 4: GMV/ISON campaigns
  GMV and ISON have cooperated in dedicated optical campaigns in 2016 (Apr, May, Jun, Jul) and 2017 (Apr) (list per satellite-group):
    A1, B1 07/04/2016-18/04/2016  station calibration
    B2 15/04/2016-20/04/2016  station calibration and manoeuvre estimation
    C2 09/05/2016-17/05/2016  station calibration
    D2, D3 06/05/2016-17/05/2016  station calibration
    E1, E2, F1 31/05/2016-08/06/2016  collision avoidance (proof-of-concept)
    B3 08/06/2016-16/06/2016  collision avoidance
    D1, D4 26/06/2016-08/07/2016  station calibration
    G1, G2 01/07/2016-08/07/2016  station calibration and manoeuvre estimation
    M7 01/04/2017-10/04/2017  de-orbiting operations of Meteosat-7
    H1 12/04/2017-21/04/2017  station calibration during IOT
  ISON sub-network used providing commercial services
  Processing performed by GMV with in-house software:
    catmai  optical data correlation (from survey telescopes)
    sstod  orbit determination with optical and ranging data, station bias calibration and manoeuvre estimation
    closeap  conjunction detection and collision risk evaluation

## Slide 5: Orbit determination
  GEO operators use ranging stations for orbit determination purposes
  Ranging data from 2 stations with different longitudes are normally used
  Optical telescopes can provide angular data, quite complementary to ranging data
  Data fusion as part of orbit determination
  Optical-only orbit solutions are also possible
  Potential use in nominal and non-nominal operations (LEOP, manoeuvres, station unavailability)

## Slide 6: Orbit determination
  ISON optical telescopes have been used for OD:
    With optical measurements only (optical-only OD)
    In combination with ranging data (data fusion OD)
    Estimating manoeuvres if executed (indicated with * below)
  Main results:
    Varying number of sensors used (optical/ranging)
    Optical data residuals RMS around 1 arcsec (0.27 millideg)
Satellite ID | Optical |  | Range |  | Optical-only OD residuals |  | Data fusion OD residuals |  | 
 | Sensors | Obs. # | Stations | Obs. # | R. A. RMS [mDeg] | Dec. RMS [mDeg] | R. A. RMS [mDeg] | Dec. RMS [mDeg] | Range RMS [m]
A1 | 4 | 1184 | 2 | 408 | 0.27 | 0.22 | 0.28 | 0.22 | 3.6
B1 | 4 | 989 | 2 | 144 | 0.26 | 0.23 | 0.28 | 0.23 | 5.2
B2* | 4 | 460 | 2 | 94 | 0.25 | 0.22 | 0.27 | 0.22 | 2.2
C2 | 9 | 2024 | 4 | 176 | 0.27 | 0.25 | 0.27 | 0.25 | 7.4
D2 | 7 | 3281 | 2 | 239 | 0.22 | 0.18 | 0.22 | 0.18 | 1.9
D3 | 7 | 3671 | 2 | 241 | 0.21 | 0.19 | 0.21 | 0.19 | 1.0
F1* | 8 | 1028 | 2 | 215 | 0.24 | 0.25 | 0.27 | 0.29 | 5.1
D1 | 9 | 1302 | 2 | 251 | 0.25 | 0.21 | 0.25 | 0.21 | 0.9
D4 | 7 | 1472 | 2 | 286 | 0.22 | 0.20 | 0.22 | 0.20 | 1.8
    Orbit determination statistics

## Slide 7: Ranging station calibration
  Ranging stations used by GEO operators are affected by biases
  These biases impact orbit determination solutions with an along track orbital bias
  Uncalibrated stations degrade orbital solutions and increase collision risk uncertainty
  Ranging stations thus need accurate calibration (~1m)
  One way of performing the calibration is the data fusion with optical data obtained from the ISON network
 | Orbital Biases [m] |  | 
 | Radial | Along-track | Cross-track
 | 1.4 | 352.8 | -2.8
 | 2.2 | 238.9 | -2.9
 | -6.6 | 472.5 | -6.6
 | 3.0 | 221.0 | -4.2

## Slide 8: Ranging station calibration
  Orbit comparisons show benefits of ranging station calibration
    a) Orbit estimated with ranging data using operator biases
    b) Orbit estimated with data fusion using calibrated biases
    c) Orbit estimated with ranging data using calibrated biases
  Biases depend on software/models  calibration must be performed with operator’s flight dynamics system
Satellite ID | Provided Range Bias vs Data Fusion (b vs a) Mean [m] |  |  | Estimated Range Bias vs Data Fusion (c vs a) Mean [m] |  | 
 | Radial | Along-track | Cross-track | Radial | Along-track | Cross-track
A1 | 0.0 | 410.2 | 0.5 | 0.1 | 3.6 | -0.5
B1 | -1.5 | -862.6 | 0.1 | 1.5 | 32.9 | -0.1
B2* | -0.1 | 2598.0 | 1.5 | 0.5 | 16.3 | -2.1
C2 | 6.5 | -784.0 | 0.3 | -6.6 | 229.2 | -0.5
D2 | 0.2 | 583.8 | 0.6 | 0.0 | 31.0 | -0.6
D3 | -4.3 | 727.5 | 0.2 | 0.0 | 1.9 | -0.3
F1* | -1.1 | 465.1 | -28.6 | 1.5 | 9.6 | 29.4
D1 | -5.9 | 843.9 | 10.1 | -0.1 | -7.0 | 0.7
D4 | 0.0 | 590.2 | 0.2 | -0.3 | -2.5 | -0.3

## Slide 9: Collision risk evaluation
  GEO satellites have high-risk collisions with space debris orbiting the GEO regime
  ~ 2-3 events per year and satellite require refined analysis with current population
  Refinement may be performed with optical tracking campaigns on target and chaser, to ensure same processing in both orbit solutions
Chaser ID | Optical |  | Optical data residual | 
 | Sensors | Obs. # | R. A. RMS [mDeg] | Dec. RMS [mDeg]
03431 | 3 | 116 | 0.335 | 0.416
20693 | 7 | 769 | 0.300 | 0.270
02717 | 2 | 650 | 0.219 | 0.203
 | Chaser Norad Id | Target RMS [m] | Chaser RMS [m] | TLE Prediction TCA | Estimated TCA | TLE Prediction Miss Distance [km] | Estimated Miss Distance [km]
 | 03431 | 142.0 | 178.1 | 20:15:00 | 20:15:14 | 50 | 36.5
 | 20693 | 181.8 | 213.4 | 02:53:33 | 02:53:31 | 20 | 32.6
 | 02717 | 144.2 | 133.9 | 15:58:40 | 15:58:35 | 14.5 | 15.7
  3 collision risk evaluation campaigns have been executed by GMV and ISON together

## Slide 10: Meteosat-7 end-of-life support
  EUMETSAT has recently performed de-orbiting operations on Meteosat-7
  Support needed due to the availability of only one ranging station
  GMV/ISON have provided operational support through the daily provision of:
    Optical tracking data transformed to azimuth/elevation
    Estimated orbit from data fusion of optical data provided by ISON and ranging data provided by EUMETSAT
    Estimated manoeuvres for under/over-performance analysis
    Report with main results of the operational activities
  Daily provision of predicted orbit (considering manoeuvre plan) to ISON for telescope tasking
  Processing performed by GMV with:
    catmai  optical data correlation (from survey sensors)
    sstod  orbit determination with optical and ranging data

## Slide 11: Meteosat-7 end-of-life support
  Main results of the campaign:
    15+ survey telescopes providing optical data from well before the actual de-orbiting operations until the end
    10+ tracking telescopes providing optical data during de-orbiting operations lasting initially 5 days
    More than 11000 optical observations (pairs of RA-Dec measurements) obtained by ISON for Meteosat-7 during the deorbiting operations
    Optical residual RMS in the order of 1 arcsec for all telescopes
    7 manoeuvres estimated within the same orbit determination process plus two pseudo-manoeuvres due to venting activities
    Provision of tracking data and orbital products to the EUMETSAT only few hours after local dawn for EUMETSAT OD activities
    Successful deorbiting of Meteosat-7 by EUMETSAT !

## Slide 12: Meteosat-7 end-of-life support
    Animated GIF of Meteosat-7 generated by CrAO observatory during the de-orbiting phase

## Slide 13: Conclusions
  ISON and GMV have been cooperated in several optical campaigns in a very fruitful way
  ISON network has shown high-availability, high-accuracy and high flexibility in terms of telescope dedication, provision of additional available survey data, and reaction against bad weather conditions
  ISON optical data and GMV processing in combination have been proved to be successful in operational campaigns
  Several scenarios have been executed:
    Orbit determination with data fusion
    Ranging station calibration
    Collision risk evaluation
    End-of-life operations
  More operational campaigns are on-going and coming

## Slide 14
Thank you
D. Escobar, PhD
F. Ayuga
A. Antón
A. Águeda
I. Molotov