## Slide 1: IMPROVEMENT OF SPACE DEBRIS MODEL IN MEO AND GEO REGIONS ACCORDING TO THE CATALOG OF KELDYSH INSTITUTE OF APPLIED MATHEMATICS (RUSSIAN ACADEMY OF SCIENCES) PhD I. Usovik, D. Stepanov, PhD V. Stepanyants, PhD M. Zakhvatkin, I. Molotov Dr. Prof. A. Nazarenko
7-th European Space Debris Conference
2017
ЦНИИМАШ
TSNIIMASH

## Slide 2: KIAM RAS catalog
For the beginning of 2017, in the catalog TsSITO KIAM RAS orbits 2190 space objects (SO) on GEO, 2635 SO on HEO and 338 SO on MEO are supported
The KIAM RAS catalog contains the fullest information about objects on high orbits
ЦНИИМАШ
TSNIIMASH
Figure 1 – Observatory fills data TsSITO
Figure 2 – Number of measurements coming to TsSITO

## Slide 3: General provisions of the SDPA model
1. Objects lager than 1 mm in size are considered.
2. Altitude-latitude distribution of spatial density catalogued SO, and statistical distributions of value and direction of their velocity are under construction on basis SO catalog.
3. The assumption that all small particles of space debris which are and crossing MEO and GEO regions, were generated as a result of explosions and destructions is used.
4. Dependence number generated particles on their sizes pays off with use of k(>d) relation number of particles the size lager d to number catalogued SO.
5. Maximum ΔV of particles at explosion depends from their mass, have a random values and equiprobable possible directions.
6. The ratio between sizes of particles and their mass is accepted fixed, according to data of table 1.
ЦНИИМАШ
TSNIIMASH
j | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
dj, сm | 0.1 | 0.25 | 0.5 | 1.0 | 2.5 | 5.0 | 10 | 25 | 75
kd (>d) | 4 104 | 3.5 103 | 5.5 102 | 88 | 20 | 7.2 | 3.2 | 2.0 | 1.0
m, kg (dj,j+1) | 8.6 10-6 | 5,8 10-5 | 2.8 10-4 | 1.8 10-3 | 0.01 | 0.064 | 0.40 | 5.0 | 1750
Table 1 - Average mass of SD different sizes
Figure 3 – Distributions of perigee and apogee altitude SD different sizes after explosion on GEO

## Slide 4: Characteristics of catalogued objects in GEO region
Figure 4 – Dependence of inclination (period) for known and unknown SO
(unknown)
Figure 5 – Dependence inclination(RAAN)
(known)
On figures dependences of inclination(period) for known (with the international number) and unknown (without the international number) objects in the catalog are represented.
ЦНИИМАШ
TSNIIMASH

## Slide 5: Characteristics of catalogued objects in GEO region
Figure 6 – Histograms of average magnitude
Figure 7 – Histograms of average relation area to mass
(unknown)
(known)
(unknown)
(known)
ЦНИИМАШ
TSNIIMASH

## Slide 6: Estimation cumulative number of SO in GEO protected region
Estimation of hit frequency catalogued objects to GEO protected region and to functioning region of geostationary S/C is carried out.
By results of calculation with use of high-accuracy model on an interval of 15 days at the protected region constantly there are 758 objects, 138 from which are launched approximately till 1990.
The amount of the objects crossing the protected region at least once during this time exceeds 2450.
Figure 8 – Time spent share assessment in GEO protected region
Figure 9 – For objects launched till 1990
ЦНИИМАШ
TSNIIMASH

## Slide 7: Large SO in GEO protected region
Dependence inclination (RAAN) for known SO launched till1990 in GEO protected region is presented
Figure 17 – SO with NORAD numbers < 20000 (till 1990)
ЦНИИМАШ
TSNIIMASH

## Slide 8: Verification SDPA model for GEO region
Figure 10 – Dependence N(>d)
Figure 11 – Coefficients k(>d)
ЦНИИМАШ
TSNIIMASH
Estimates of S/m and magnitude allow to estimate the size and mass of fragments approximately. For calculation of magnitude (m) of d, spherical SO diameter, and albedo ρ at range of R at zero phase coal the formula is used
where ρ = 0.09-0.12 for fragments of space debris and ρ = 0.2 for S/C and upper stages. Known magnitude of SO allows to calculate diameter of object and its visible area
The knowledge of the area and relation area to mass provides possibility of determination mass of object
The estimates of number of objects depending on their sizes constructed on the basis of magnitude estimates according to the catalog including known and unknown objects in the GEO region are presented on right figures.

## Slide 9: Improvement model distributions of orbital parameters
For improvement distributions of spatial density and velocity of SD 10-75 cm in GEO region rated distributions of perigee altitudes and inclinations of unknown SO in the catalog are constructed. Dependence of eccentricity on perigee altitude is considered on a formula
where Δej – evenly distributed random variable having the range of values in interval ≈ ±0.05. In all cases of ej ≥0. For construction spatial density Δej pays off with the random number generator.
Figure 12 – Distribution of perigee altitudes
Figure 13 – Distribution of inclinations
ЦНИИМАШ
TSNIIMASH

## Slide 10: Improvement of spatial density distribution SD 10-75 cm in GEO region
Rated distribution of spatial density SD 10-75 cm are presented on figure 14.
A characteristic feature of construction altitude-latitude spatial density distribution feature size 10-75 cm with the use of a rated spatial density is the independence from the size of the fragments. Therefore, this distribution can be represented as follows:
Figure 14 – Rated distribution of spatial density for SD 10-75 cm
k | 5 | 6 | 7 | 8
, см | 2.5 – 5.0 | 5.0 - 10 | 10 - 25 | 25 - 75
 | 2.593 10-9 | 8.506 10-10 | 2.551 10-10 | 2.126 10-10
 | 15900 | 4872 | 1461 | 1218
Table 2 – Maximum spatial density and estimation number of SD in GEO region
ЦНИИМАШ
TSNIIMASH

## Slide 11: Improvement of SD velocity distributions in GEO region
With use of the techniques developed earlier, distributions of size and the directions of velocity concerning the direction on the East for two groups of objects are constructed. They are presented in figures 15 and 16.
The bigger dispersion of velocity values is characteristic of SD smaller than 75 cm and essential distinctions of distributions of the velocity vector direction.
Figure 15 –Distribution of vector velocity directions
Figure 16 – Distribution of velocity values
ЦНИИМАШ
TSNIIMASH

## Slide 12: Estimation of mutual collision in GEO region
ЦНИИМАШ
TSNIIMASH
With use of the mutual collisions estimation technique developed earlier, the estimation of mutual collisions probability in the region 35700-35900 km on altitude and ± 1 degree on latitude for cataloged SO (> 75 cm) with SO of the different sizes is carried out. Results of estimation are presented in table 3.
From these results it is visible that the probability of mutual collisions of the catalogued SO (>75 cm) makes 0.00627 in a year. It means that the average interval between such collisions is equal ≈ 160 years, at current population of SD in GEO region. Probabilities of collisions catalogued SO with objects from 2.5 cm to 75 cm in size are 2-3 orders less.
j | 5 (2.5-5 cm) | 6 (5-10 cm) | 7 (10-25 cm) | 8 (25-75 cm) | 9 (>75 cm)
P (j,9) | 0.0002678 | 0.0000258 | 0.0000032 | 0.0000026 | 0.00627
Table 3 – Estimation of year collision probability for objects different size

## Slide 13: Improvement SDPA model in MEO region
Figure 18 – Altitude (Inclination), 2017
Figure 19 – Inclination (RAAN), 2017
ЦНИИМАШ
TSNIIMASH
Figure 20 – Spatial density in GNSS region
Table 5 – Estimation SD different sizes

## Slide 14: Velocity distributions in GNSS region
ЦНИИМАШ
TSNIIMASH
Figure 21 – Distributions of transversal and radial velocity
Figure 22 – Azimuth distributions of transversal velocity

## Slide 15: Offers on measurements for SD model calibrations
ЦНИИМАШ
TSNIIMASH
Figure 23 – Histogram of GEO SO magnitude in experimental measurements
Figure 25 – Distribution of objects angular coordinate in experimental measurements
Figure 24 – Distribution of phase angles of experimental measurements in GEO region
Figure 26 – Histogram of object size
estimations

## Slide 16
141070, Moscow region, Korolev, Pionerskaya str. 4
@:usovikiv@tsniimash.ru; phone: +7 (495) 513-50-13
www.tsniimash.ru
ЦНИИМАШ
TSNIIMASH
Conclusions
The analysis of TsSITO KIAM RAS catalog is carried out
With use of the catalog data SD model parameters are improved.
The estimation of probability of mutual collisions in the vicinity of a maximum of spatial density protected GEO region is carried out.
The analysis of experimental measurements for verification of SDPA model is carried out.
http://www.iki.rssi.ru/books/2013nazarenko.pdf